## Slide 1
Methods
Conclusions
Measurement-Oriented Microscopy Reconstruction
for Cross-Magnification Micro-Displacement Inspection
Bibliography
Introduction
Results
Paper Code: TW0243
Yen Hsuan Chiang, Liang-Chia Chen*
Department of Mechanical Engineering, National Taiwan University
No. 1, Sec. 4, Roosevelt Rd., Taipei 10617, Taiwan. *Correspondence: lchen@ntu.edu.tw
Micro-displacement inspection requires image features that can be located consistently when the objective changes. Optical blur and pixel sampling affect the boundary signals used to estimate position.
MOSR combines calibrated optical guidance, anti-aliased multiscale features [1,2] and bounded correction on the original pixel grid. One fixed set of reconstruction weights serves 20× and 50×. We test its measurement benefit using the same circle-center procedure for Raw, fixed Wiener and MOSR.
Raw
MOSR
20×
2 µm
2 µm
50×
2 µm
2 µm
Fig. 1. Corresponding Raw and MOSR fields at both objectives. Paired images share the crop and grayscale range. Scale bars: 2 µm.
Optically guided reconstruction on the native grid
Input
image
Anti-aliased
multiscale features
Native-grid
refinement
Input-referenced
bounded output
Calibrated optical guidance
Original-image reference
Fig. 2. Functional design of MOSR. Calibrated guidance addresses optical variation; anti-aliased features target sampling sensitivity. Refinement and bounded output retain the native image grid.
Common readout for Raw, fixed Wiener and MOSR
c
LSC centers
in paired frames
Median shift
of nine pillars
30 single steps
Sample SD
Boundary points and LSC center
Fig. 3. Measured boundary points [3] and a fitted circle center [4] feed the shared displacement readout. The inset uses an actual MOSR frame.
TABLE I. EVALUATION AT A 1 µm NOMINAL STEP
Objective | Acquisition | Steps | µm/pixel
20× | 31-frame evaluation scan | 30 | 0.1725
50× | 30 locked adjacent pairs | 30 | 0.0690
Centers come from maximum-gradient boundary points and geometric LSC fits. Nine-pillar median shifts use the acquisition direction. Each condition reports the sample SD of 30 steps (denominator 29).
At a common nominal step of 1 µm, MOSR gives the lowest observed Step SD in both evaluations. Each comparison uses the same images and measurement settings for all three methods.
20×, 1 µm: 30 single steps
57.2%
MOSR Step SD
4.068 nm
Lower Step SD relative to Raw
Step SD (nm) | Raw | Wiener | MOSR
 | 9.506 | 5.794 | 4.068
Chart: Step number
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
Raw | -5.5006 | -5.9084 | 2.6995 | 4.1069 | 8.6555 | 2.3965 | -8.5655 | 0.50842 | 12.6509 | -5.7355 | 11.7848 | -26.0693 | 5.6064 | 10.0253 | -11.4786 | 20.235 | -8.7597 | -4.1751 | 10.5609 | -5.8781 | 4.0199 | 3.7729 | 4.2599 | 0.61785 | 7.1367 | 0.21894 | 9.489 | 11.022 | -10.847 | 9.7751
Wiener | 1.2162 | 2.7172 | -5.0176 | -4.7975 | -6.4943 | 8.0349 | 2.3345 | -0.051228 | -4.9412 | -2.722 | 5.5867 | 6.5633 | 2.9122 | 2.0684 | -1.4306 | 2.4327 | 17.393 | 9.439 | 7.8415 | -1.5315 | 2.7029 | -0.045107 | 12.3826 | -0.034985 | 0.03399 | -3.4392 | 11.2832 | -2.53 | 1.6233 | -5.1788
MOSR | -3.2279 | 2.711 | -2.7459 | -10.3681 | -3.9246 | 9.6615 | -1.8698 | -3.6535 | 2.0791 | 1.7639 | -0.20951 | 6.0874 | 0.2095 | 2.5216 | 4.6349 | 5.6154 | 0.2586 | 1.5373 | 1.8375 | 1.1707 | 1.5935 | 1.4932 | 5.0604 | -2.3249 | 8.5974 | 4.2866 | 0.36311 | 5.2617 | 4.0812 | 1.1231
Fig. 4. All 30 single-step displacements at 20×. Curves use measured step minus 1 µm, with the same axis limits as the 50× evaluation.
At 20×, the mean step changes by only 0.10 nm while Step SD decreases by 5.44 nm. The dominant observed change is lower dispersion around a similar mean.
50×, 1 µm: 30 single steps
23.5%
MOSR Step SD
4.542 nm
Lower Step SD relative to Raw
Step SD (nm) | Raw | Wiener | MOSR
 | 5.938 | 4.722 | 4.542
Chart: Pair number
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
Raw | 2.6864 | 9.1825 | 2.1385 | 19.0385 | 7.5524 | 8.2925 | 1.9384 | 0.16976 | 12.5169 | -7.5246 | 7.5557 | -6.0163 | 2.9378 | 4.85 | -1.9919 | 7.0065 | 10.3856 | 4.3704 | -4.6052 | 1.7295 | 6.64 | 2.9528 | 1.5653 | -1.8421 | 11.0021 | 7.2659 | -3.047 | 12.2517 | 1.9229 | 4.4843
Wiener | 0.77691 | 9.5928 | 0.73385 | 9.536 | 6.0438 | 8.9378 | 5.0386 | -2.235 | 8.7416 | -9.1882 | 4.837 | 2.3155 | 0.54845 | 0.92233 | 1.6564 | 7.4694 | 8.8941 | 1.794 | -7.0049 | 0.58665 | 6.6263 | 1.4774 | 1.9809 | 2.5077 | 3.5725 | 8.7267 | 3.9027 | 10.3701 | 7.7915 | 4.2995
MOSR | 0.68023 | 12.2429 | 1.8637 | 12.5647 | 5.4357 | 7.2084 | 4.6233 | -1.3055 | 7.424 | -7.9767 | 3.4927 | -1.5366 | 0.76876 | 0.78268 | -0.28674 | 4.945 | 9.1927 | 1.0557 | -5.1531 | -0.64555 | 6.0376 | 0.46536 | 4.1592 | 3.2941 | 2.3063 | 6.3042 | 2.7821 | 8.7737 | 3.9204 | 2.0864
Fig. 5. All 30 locked single-step displacements at 50×. MOSR reaches 4.542 nm Step SD with the same learned weights and the corresponding optical calibration.
With shared reconstruction weights and objective-specific optical guidance, MOSR reduces single-step variation by 57.2% at 20× and 23.5% at 50×. The observed reductions under a common center readout support MOSR for cross-magnification micro-displacement inspection.
[1] O. Ronneberger et al., U-Net, MICCAI, 2015, pp. 234–241.
[2] R. Zhang, Making convolutional networks shift-invariant again, ICML, 2019, pp. 7324–7334.
[3] T. F. Chan and L. A. Vese, Active contours without edges, IEEE Trans. Image Process., 10(2), 266–277, 2001.
[4] N. Chernov and C. Lesort, Least squares fitting of circles, J. Math. Imaging Vis., 23, 239–252, 2005.
Notes: IMPACT2026 TW0243. Public model name: MOSR. This poster presents an updated evaluation at a nominal 1 micrometer step. The 20x condition uses one complete 31-frame evaluation scan; the 50x condition uses its fixed prior list of 30 adjacent-frame pairs. Conditions are reported separately. All methods use the same image pairs, identities, scale and center-estimation procedure within each condition. Fig. 2 is a functional overview, not an isolated-component efficacy result. Fig. 3 uses measured boundary points and a fitted center from the displayed 20x MOSR field. The curves contain all 30 observed displacements per condition and method, minus nominal 1000 nm for display; no per-method centering, detrending or smoothing is applied. Sources for method context: Ronneberger et al., MICCAI 2015; Zhang, ICML 2019; Chan and Vese, IEEE TIP 2001; Chernov and Lesort, JMIV 2005.